Bold Face Procedures are immediate action items & should be committed to memory.  In any abnormal or emergency situation, Maintain Aircraft Control, Analyze the Situation & take Appropriate action. Refer to the aircraft POH as the amplified procedures are a significant source of information.  Land as soon as practicable.

If forced landing or other emergency is encountered, consider changing squawk to 7700 and transmitting a MAYDAY call after completion of the required checklist

ENGINE FIRE ON START

- Cranking	CONTINUE

If engine starts:

- Power	1700 RPM  for a few mins.

- Engine	SHUTDOWN

If engine fails to start:

- Cranking	CONTINUE

- Throttle	FULL OPEN

- Mixture	IDLE CUTOFF

- Fire Extinguisher	OBTAIN

- Engine	SECURE

- Fire	EXTINGUISH

ABORT

- Throttle	IDLE

- Brakes	APPLY

ENGINE FAILURE DURING TAKEOFF ROLL

- ABORT

- Flaps	RETRACT

- Mixture	IDLE CUT-OFF

- Ignition Switch	OFF

- Master Switch	OFF

ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF

- Airspeed	60 KIAS

- Mixture	IDLE CUT-OFF

- LAND STRAIGHT AHEAD

If time permits

- Fuel Selector Valve	OFF

- Ignition Switch 	OFF

- Flaps	AS REQUIRED

- Master Switch	OFF

ENGINE FAILURE DURING FLIGHT

- Airspeed	60 KIAS

- Fuel Valve	ON

- Mixture	RICH

- Throttle	FORWARD

- Carburetor Heat	ON

- Primer	IN and LOCKED

- Ignition Switch	BOTH or START (if propeller stopped)

EMERGENCY LANDING WITHOUT ENGINE POWER

      - Airspeed	65 KIAS (Flaps UP)

60 KIAS (Flaps DOWN)

      - Landing Field	SELECT

      - Fuel Selector	OFF

      - Transponder	SET 7700

      - Radio Call	MAYDAY ON ACTIVE FREQ or. 121.5

      - Mixture	IDLE CUTOFF

      - Ignition Switch	OFF

      - Seatbelts	SECURE & TIGHT

      - Flaps	30º on Final Approach

      - Master Switch	OFF

      - Doors	UNLATCH PRIOR TO TOUCHDOWN

      - Touchdown	SLIGHTLY TAIL LOW

      - Brakes	APPLY HEAVILY (DO NOT LOCK BRAKES!)

PRECAUTIONARY LANDING WITH ENGINE POWER

- Airspeed	60 KIAS

- Flaps	20º

- Selected Field	OVERFLY

- Avionics & Electrical Systems	OFF

- Flaps	30º (On Final Approach)

- Airspeed	55 KIAS

- Master Switch	OFF

- Doors	UNLATCH PRIOR TO TOUCHDOWN

- Touchdown	SLIGHTLY TAIL LOW

- Ignition Switch	OFF

- Brakes	APPLY HEAVILY

ENGINE FIRE IN FLIGHT

- Mixture	IDLE CUTOFF

- Fuel Valve	OFF

- Master Switch	OFF

- Cabin Heat	OFF

- Air Vents	CLOSED

- Airspeed	100 KIAS

- Forced Landing	EXECUTE

ELECTRICAL FIRE IN FLIGHT

- Master Switch	OFF

- Avionics	OFF

- All other switches (except ignition switch)	OFF

- Vents/Cabin Air/Heat	CLOSED

- Fire	EXTINGUISH

CABIN FIRE

- Master Switch	OFF

- Vents/Cabin Air/Heat	CLOSED

- Fire	EXTINGUISH

- Land as soon as practicable

WING FIRE

- Navigation Lights	OFF

- Pitot Heat	OFF

Sideslip to keep the flames from fuel tank and cabin

- Land as soon as possible

LANDING WITH FLAT MAIN TIRE

- Flaps	AS DESIRED

- Approach	NORMAL

- Touchdown	GOOD TIRE FIRST

hold airplane off flat tire as long as possible

INADVERTENT ICING ENCOUNTER

- Pitot Heat Switch	ON

- Carb Heat	ON

- Turn Back or Change Altitude

- Cabin heat	FULL ON

- Defroster outlets	OPEN to max

- Throttle	Increase minimize ice build up on propeller blades

- Land as soon as Practicable (Possible)

STATIC SOURCE BLOCKAGE

- Static Pressure Alternate Source Valve	PULL ON

EXCESSIVE RATE OF CHARGE

- Avionics Power Switch	OFF

- Master Switch	OFF (Both sides)

- Master Switch	ON

If overvoltage light illuminates again:

- Alternator Circuit Breaker	PULL

- Non-essential Electrical equipment	OFF
Flight	TERMINATE as soon as practical

LOW-VOLTAGE LIGHT INFLIGHT

- Master Switch (Both Sides)	OFF

- Master Switch	ON

If over-voltage light illuminates again;

- Flight	TERMINATE

AMMETER SHOWS DISCHARGE

      - Alternator	OFF

      - Nonessential Electrical Equipment	OFF

- Flight	TERMINATE

SPIN RECOVERY

- AILERONS	NEUTRAL

- THROTTLE	IDLE

- RUDDER	FULL OPPOSITE DIRECTION OF ROTATION

- YOKE	FORWARD to break stall

- HOLD THESE CONTROL INPUTS UNTIL ROTATION STOPS.

- When Rotation Stops	NEUTRALIZE RUDDER

AND MAKE A SMOOTH RECOVERY FROM THE RESULTING DIVE